## Slide 1: BE Project 2011-2012 Autonomous Mapping Robot
Team : 2
Ankit Trivedi
Ankita Shrotriya
Rahul Patil
Prathamesh Akolkar

## Slide 2: Problem Statement
An Intelligent Autonomous robot (Firebird V Atmega2560)
Scanning (Servo motor, Sharp IR sensor)
Detection of obstacle, Navigation and self-localization
Serial Communication (XBee)
Mapping (Matlab)

## Slide 3: Requirements/Task Specifications
Firebird – Requires 1 bot (Atmega2560)
Servo motor (VS-1) – Used for scanning purpose with the resolution of 9°
Sharp IR sensor (GP2D12) – Measures the distance of the obstacle from the bot
XBee (XB24) – Used for serial communication from bot to host PC

## Slide 4: Project Plan
ACTIVITY | AUG’11 & SEPT’11 | OCT’11 & NOV’11 | DEC’11 & JAN’12 | FEB’12 & MARCH’12 | APRIL’12
Literature Survey |  |  |  |  | 
Study of hardware and software tools |  |  |  |  | 
Designing different algorithms |  |  |  |  | 
Gathering of hardware requirement |  |  |  |  | 
Testing of different algorithms & implementation |  |  |  |  | 
Documentation |  |  |  |  | 
Report submission |  |  |  |  | 

## Slide 5: Arena Diagram

## Slide 6: Workflow

## Slide 7: Workflow
Bot starts its operation by initializing coordinates (x,y)=(0,0) and direction D=‘N’(North).
180° scanning
  Performs scanning and takes 21 samples (r,a).
  Transmits (x,y,a,r) to host PC via XBee module(2.4 GHz).
Matrix scanning
    Takes 3 samples at 0°, 90° and 180° to determine number of blocks.
    Matrix generated
    1 No obstacle(free space)
    0 obstacle
Decides its navigation path accordingly by checking 3 conditions.

## Slide 8: Workflow
Check condition 1:
  True – move forward, scans, upgrade direction and send the data.
  False- checks condition 2.
Check condition 2 :
  Case1- turns left by 90, scans, upgrade direction and send the data.
  Case2 –turns right by 90 ,scans ,upgrade direction and send the data.
Scans every block until the co-ordinates becomes (0,0).
Transmits the complete matrix.
Ends the operation.

## Slide 9: Workflow
L | C | R | Direction of the Robot
0 | 0 | 0 | Right(2) + forward
0 | 0 | 1 | Right + forward
0 | 1 | 0 | Forward
0 | 1 | 1 | Forward
1 | 0 | 0 | Left + forward
1 | 0 | 1 | Left + forward
1 | 1 | 0 | Left + forward
1 | 1 | 1 | Left + forward

## Slide 10: Innovations and challenges
To achieve maximum efficiency and resolution.
Using two different scanning techniques simultaneously.
Integrating the samples for each block of an arena.
Real time mapping using Matlab.

## Slide 11: Task Completion
NO. | TASK | PROBLEMS | SOLUTION
1. | Range finding, obstacle detection and navigation | Interference of signals | Using only 1 sharp IR sensor
2. | No. of scanning samples | Less no. of samples (13) | Extra hardware required for PWM
3. | Merge of coding | Buffer overload(Spark Atmega16) | Spark V Atmega32
4. | Code implementation in Atmega 32 | Non-compatibility | Firebird V Atmega 2560
5. | Range calculation | Wide beam width | Sharp IR sensor with narrow beam
6. | Alignment | Wheel encoding resolution | Magnetic compass (future)

## Slide 12: Review and Test Plan
Two types of operating modes-
Mapping and Scanning 1800 scanning
Matrix Generation
Navigation Direction algorithm
(X,Y) algorithm

## Slide 13: Test Criteria
1800 scanning
  Sharp sensor mounted on servo.
  21 samples of (x,y,r,a) with angle resolution of 90.
  Transmits (x,y,r,a) for each sample to the host PC via Xbee.
  Such 21 samples are transmitted for each block via serial communication.
  Conversion from polar to Cartesian --
  p= x+r cos(a)
  q= y+r sin(a)

## Slide 14: Test Criteria
  Matrix scanning:
    Selection of three samples  00 , 900 & 1800 degrees.
    The range calculated at these angles will be divided by 20 to determine the number of blocks.
    Matrix generated
    1 No obstacle(free space)
    0 obstacle
    Logical OR of new and previous value.
    Transmits complete matrix.

## Slide 15: Test Criteria
Direction algorithm-
Predefined pointer called NUM, initially directed at ‘N’.
Whenever robot turns , the pointer will increment or decrement accordingly.
Eg-Turn right  Pointer increment
Turn left  Pointer decrement

## Slide 16: Test Criteria
    (X,Y) algorithm-
    Depending upon the direction, the robot will calculate its current block position (X,Y).
    Eg-
    North  Y increments
    South  Y decrements
    East  X increments
    West  X decrements

## Slide 17: Reusability features
Magnetic compass - To reduce the positional error.
Sensor with higher range - To increase the range of the sensor for detection of wall or an obstacle more efficiently for the larger area.
Increasing angle resolution of servo shaft - To increase the number of scanning samples taken by servo shaft.

## Slide 18: Future Enhancement
Automatic vacuum cleaning
Surveillance security systems
Operating robot by mobile phone (android application)

## Slide 19
Thank you!!